## Slide 1
16-bit, 3-Stage Pipelined ALU
Project Presentation
Decode → Execute → Writeback
A 16-bit ALU architecture demonstrating datapath design, pipelining and hazard handling
Software/RTL simulation project

## Slide 2
Project Objective
Design a 16-bit Arithmetic Logic Unit organized as a 3-stage pipeline.
Pipeline stages: Decode → Execute → Writeback.
Demonstrate overlapping instruction execution using pipeline registers.
Support arithmetic, logical, shift and compare operations.
Generate status flags: Zero (Z), Carry (C), Overflow (V), Negative (N).

## Slide 3
Supported ALU Operations
ADD — A + B
SUB — A − B
AND — A & B
OR — A | B
XOR — A ^ B
NOT — ~A
Shift Left / Shift Right
Compare — arithmetic comparison using subtraction

## Slide 4
3-Stage Pipeline Architecture
STAGE 1
DECODE
ID/EX
REGISTER
STAGE 2
EXECUTE
EX/WB
REGISTER
STAGE 3
WRITEBACK
Pipeline registers preserve in-flight instruction information between clock cycles.

## Slide 5
Stage 1 — Decode
Fetch/receive the instruction information.
Identify the opcode and source/destination operands.
Read the required 16-bit operands from the register file.
Store decoded information in the ID/EX pipeline register.
Purpose: prepare the instruction for the Execute stage.

## Slide 6
Stage 2 — Execute
Receive opcode and operands from the ID/EX register.
Perform the selected 16-bit ALU operation.
Generate the 16-bit result.
Calculate Z, C, V and N status flags.
Store result, flags and destination information in the EX/WB register.

## Slide 7
Stage 3 — Writeback
Receive the result from the EX/WB pipeline register.
Write the result to the destination register.
Commit the generated status flags.
After Writeback, the instruction has completed.
Separating Writeback allows other instructions to be decoded/executed simultaneously.

## Slide 8
Pipeline Timing Example
Example instruction sequence:
ADD R1, R2, R3
SUB R4, R5, R6
AND R7, R1, R4
Instruction | Cycle 1 | Cycle 2 | Cycle 3 | Cycle 4
ADD | Decode | Execute | Writeback | 
SUB |  | Decode | Execute | Writeback
AND |  |  | Decode | Execute

## Slide 9
Status Flags
Z (Zero): set when the 16-bit result is 0.
C (Carry): indicates carry out for addition / borrow-related comparison for subtraction.
V (Overflow): indicates signed arithmetic overflow.
N (Negative): equals the most-significant bit of the result.
Flags are produced during Execute and committed during Writeback.

## Slide 10
Data Hazard
Example dependency:
Instruction 1: ADD R1, R2, R3
Instruction 2: ADD R4, R1, R5
Instruction 2 needs R1 before Instruction 1 has completed Writeback.
This is a Read-After-Write (RAW) data hazard.
Planned solution: forwarding and/or stalling.

## Slide 11
Current Progress for Presentation
16-bit ALU architecture defined.
3-stage Decode → Execute → Writeback datapath defined.
ID/EX and EX/WB pipeline-register concept established.
Basic ALU operations and status-flag logic implemented in Verilog simulation.
Next implementation focus: complete Writeback integration and hazard handling.
Final phase: testbench, cycle-by-cycle trace and documentation.

## Slide 12
Expected Demonstration
Run a short instruction sequence in simulation.
Show the result of each ALU operation.
Show Z, C, V and N flags.
Show instructions occupying different pipeline stages in the same clock cycle.
Demonstrate a dependent instruction and explain the RAW hazard.
Explain how forwarding/stalling will resolve the hazard.

## Slide 13
3-Week Completion Plan
Week 1: complete all ALU operations, flags and 3-stage pipeline integration.
Week 2: implement RAW hazard detection and forwarding/stalling; add test cases.
Week 3: complete visualization, edge-case testing, report and final demonstration.
Final deliverables: Verilog source, testbench, pipeline trace, report and presentation.

## Slide 14
Conclusion
The project demonstrates how a 16-bit ALU can be divided into pipeline stages.
Pipeline registers allow multiple instructions to be in flight simultaneously.
The main architectural challenge after basic pipelining is data-hazard handling.
The completed simulator/RTL will provide cycle-by-cycle evidence of pipeline operation.